Count Bits Set
German Language
Aus meiner Vorlesung

---
Count Bits Set (in an Integer)
uint32_t cbs(uint32_t v){
  uint32_t c;
  // reuse input as temporary:
  v = v - ((v >> 1) & 0x55555555); //count in fields of size 2
  v = (v & 0x33333333) + ((v >> 2) & 0x33333333); //add fields of size 2 => now fields of size 4
  c = ((v + (v >> 4) & 0xF0F0F0F) * 0x1010101) >> 24; //from size4 add results to fields of size 8,
        //plus add all results of fields with size 8
        //and shift result to lowest Byte
  return c;
}
Schritt 1: Zählen in Feldern der Größe 2

---
Schritt 2:	Felder der Größe 2 zusammenfassen
zu Feldern der Größe 4
Zählen in dunkel-
grauen Feldern
Zählen in hell-
grauen Feldern
zusammenzählen

---
Schritt 3:	Felder der Größe 4 zusammenfassen
zu Feldern der Größe 8

---
Schritt 4:	4 Felder der Größe 8 zusammenfassen
zu Feld der Größe 32
Endergebnis

---
Vergleich von Lösungen des Problems
X68 Assembler
maskierender Vergleich
„paralleles“ Zählen

---
Vergleich von Lösungen des Problems
Benchmarking Algorithms for "Count Set Bits"
Running all Algorithms with Input from 0 to 4294967295...
Algorithmus 0: 69 Parallel -> Version of CountBitsSet
Algorithmus 1: 71 Parallel 2 -> Version of CountBitsSet
Algorithmus 2: 154 Nibble LUT -> Nibble only
Algorithmus 3: 140 Nibble LUT2 -> 2 Nibbles of a Byte at once
Algorithmus 4: 93 Nubble LUT Unrolled -> Access Bytes by shifts
Algorithmus 5: 110 Nubble LUT Unrolled2 -> Access Bytes via union
Algorithmus 6: 291 briankernighansway -> Human readable Algorithm
Dauer in Sekunden